Bilkent University
Computer Science
CS 224 (Computer Organization)
Lab 5 Design Report

Section 2
Barkın Saday
21902967
12.04.2022

Part B & C: List of Possible Hazards and Solutions

Control Hazards:

Branch hazard:

-Reason: When the next instruction is fetched from the instruction memory if the branch decision is not yet made it will cause this hazard.

-This hazard can occur when a branch decision is needed

-Pipeline Stages That are Affected: If branch prediction is wrong 3 unnecessary instruction will be fetched since there is a delay in branch prediction.

-Solution: Stalling. We can stall the pipeline for 3 cycles. Another solution can be making the branch decision early. However, the second solution will require additional hardware implementation.

Data Hazards:

Load-Use Hazard:

-Reason: Reading from memory can not be done until the end of the Memory Stage. So, instructions that need reading from memory does the reading at the end of Memory Stage. However, in that case the next instruction can not access the data during the Execute stage.

Pipeline Stages That are Affected: If we need to do a writing to memory, Execute and Memory stages can be affected by the delay of these two cycle. So hazard can occur if consecutive instructions tries to access data in the memory.

-Solution: Stalling is a way of of solving. We can hold the pipeline until data is available.

Load-Store Hazard:

-Reason: Trying to store data in memory right after loading the data from memory. For example, using “lw” and “sw” one after the other with the exact same target register.

-Pipeline Stages That are Affected: Since wrong data will be stored in memory location memory stage of the “store” instruction will be affected.

-Solution: Stalling until next instruction fetches data from the register (which is the same register) at the decoding stage.

Compute-Use Hazard:

-Reason: Next instruction can read the wrong data from the previous instruction since the computed data is not yer written (because it is written at the end of Write Back Stage)

-Pipeline Stages That are Affected: WriteBack and Execute Stages of the next instruction is affected since these stages will be performed by the wrong data value.

-Solution: Forwarding is a good way for solving this problem. Data can be forwarded to the next instructions Execute Stage to perform operation with the correct value. By forwarding we do not need to wait for the WriteBack Stage.

Part D: Logic Equations for Hazards

Stalling:

lwStall = ( ( rtD = = rtE ) | | ( rsD == rtE ) ) && MemToRegE StallF

Forwarding:

if( rsE == WriteRegMem) && ( rsE != 0 ) && RegWriteM
ForwardAE = 10

else if ( rsE == WriteRegMem) && ( rsE != 0) && !RegWriteM
ForwardAE = 01

else
ForwardAE = 00

Part E: SRAAC Hazards and Testing

-Since we are doing sequantial loading and writing to the memory “load-store” hazards can occur. The reason is explained in the “load-store” hazard’ reason part.

We make computations in the data which we are writing to memory. So “compute-use” hazards can occur due to the reasons stated above.