CS224 / Lab 7.
Sec 2	Sec 2
Utku Kurtulmus Barkın Saday
ID:21903025	ID:21902967

PART2_B
SFRs
I-O Devices
A DC motor->PORTA, TRISA, LATA
2 Button Switches ->PORTE, TRISE, LATE

       b) code

#include <P32.xxxx.h>

//DC motor
// J4: Control1 : 10, MOTOR1:3
// Control2 : 2, MOTOR2:6

//Push Buttons
//J1 Button0 : 1
// Button1 : 10

void main() {

AD1PCFG = 0xFFFF; // Configure AN pins as digital I/O
JTAGEN_bit = 0; // Disable JTAG

TRISE = 0xFFFF //portE inputs(switch buttons)
TRISA = 0x0000 //portA outputs for DC motor

LATA = 0Xffff; //default values
LATE = 0X0000; //default values

while(1) {
  if(PORTEbits.RB0 & PORTEbits.RB1) { //if you push two button at the same time, no turn
  PORTAbits.CONTROL1 = 0;
  PORTAbits.CONTROL2 = 0;
  }
  else{
  PORTAbits.CONTROL1 = PORTEbits.RB0; //if you push button 0(RB0) turn counter-clockwise
  PORTAbits.CONTROL2 = PORTEbits.RB1; //if you push button 1(RB1) turn clockwise
  }
}

}

PART2_C

c) SFRs
I-O Devices
Seven Segment Module--> > D->TRISA, PORTA,
        AN->TRISE, PORTE
d) code
/*
Configuration for the code below:

Connect portA to J1 Port of 4 Digit Seven Segment Module
Jumpers of portA are : 5V, pull down ( top one to left, other to right )

Connect portE to J2 Port of 4 Digit Seven Segment Module
Jumpers of portE are : 5V, pull down ( top one to left, other to right )
*/

// Hexadecimal values for digits in 7 segment
unsigned char binary_pattern[]={0x3F,0x06,0x5B,0x4F,0x66,0x6D,0x7D,0x07,0x7F,0x6F};

void main() {

AD1PCFG = 0xFFFF; // Configure AN pins as digital I/O
JTAGEN_bit = 0; // Disable JTAG

TRISA = 0x00; //portA is output to D
TRISE = 0X00; //portE is output to AN

int i = 1;
while(1)
{
     //Digit1
     PORTA=binary_pattern[i % 10];
     PORTE=0x01;
     Delay_ms(1);

     // Digit 2
     PORTA=binary_pattern[(i + 1) % 10]; // Put 2 to the second digit
     PORTE=0x02; // Open second digit
     Delay_ms(1);

     // Digit 3
     PORTA=binary_pattern[(i + 2) % 10];
     PORTE=0x04;
     Delay_ms(1);

     // Digit 4
     PORTA=binary_pattern[(i + 3) % 10];
     PORTE=0x08;
     Delay_ms(1);

     Delay_ms(1000); // wait 1 second
     i++;
}

}//main

PART2_D
e) SFRs

I-O Devices
8 LED outputs → LATA , TRISA
3 Button Switches → PORTE, TRISE

f) code
void main() {
AD1PCFG = 0xFFFF;
JTAGEN_bit = 0;
TRISA = 0; //PORTA is output for LEDs
TRISE = 1; //PORTE is input to read push-buttons
int speed = 1000; // one second (default), make it smaller for faster demonstration
Delay_ms(speed);
int c = 0 //counter
LATA = 0xffff; //LEDs off by default
LATE = 0x0000;
//Loop
while(1)//always keep going
{
PORTE = 0x0000;//reset push-buttons
if(PORTEbits.RF2 == 1)//reset is pressed
{
LATA = 0b11111111;
c = 0;
continue;
}
//1 is pressed, 0 is unpressed
if(PORTEbits.RF0 == 1 && PORTEbits.RF1 == 1) //if both pressed, ignore
{
continue;
}
else if(PORTEbits.RF0 == 1)//left to right (RF0 is pressed)
{
LATA = c % 128;
c++;
}
else if(PORTEbits.RF1 == 1)//right to left (RF1 is pressed)
{
LATA.F0 = ((c % 128) & 0b10000000) != 0;
LATA.F1 = ((c % 128) & 0b01000000) != 0;
LATA.F2 = ((c % 128) & 0b00100000) != 0;
LATA.F3 = ((c % 128) & 0b00010000) != 0;
LATA.F4 = ((c % 128) & 0b00001000) != 0;
LATA.F5 = ((c % 128) & 0b00000100) != 0;
LATA.F6 = ((c % 128) & 0b00000010) != 0;
LATA.F7 = ((c % 128) & 0b00000001) != 0;
c++;
}
Delay_ms(speed);
}
}//end of main